## Slide 1: Overview Of ORION (ARTEMIS-II) S-band Doppler Tracking
Deep Space Exploration Society (DSES) Station: Haswell 18.2 m Dish Frequency: 2216.5 MHz (S-band)
Presenter: Alex K6VHF

## Slide 2: MISSION OVERVIEW
The ARTEMIS-II mission is NASA’s first crewed Orion flight in the Artemis program, launched April 1, 2026, with a ~9-day translunar trajectory.

## Slide 3: DSES INVOLVMENT
The DSES station is one of 39 ground stations worldwide selected to track the ARTEMIS-II Orion spacecraft and record Doppler data.
The DSES station conducted passive one-way Doppler tracking of the Orion spacecraft carrier signal during multiple tracking windows between:
April 4, 2026 April 8, 2026 April 9, 2026
Tracking was performed using:
18.2 m parabolic dish (f/D = 0.42)
Low-noise S-band front-end (~0.5 dB NF)
SDR platform (USRP / B200/B210)
Rubidium 10 MHz reference

## Slide 4: MEASUREMENT METHODS
Signal Processing Chain
Center frequency near: 2216.5 MHz
FFT-based spectral processing
Doppler extraction via: - Peak detection - Quadratic interpolation - Optional centroid/phase methods
Output Format - CCSDS TDM v2.0 - Observable:
RECEIVE_FREQ_2 = Doppler offset (Hz)
Reference Data
JPL Horizons ephemeris (range & range-rate) used as truth model
LINK: https://ssd.jpl.nasa.gov/horizons/app.html#/
All scripts were written in python and available for everyone.

## Slide 5: DISH FEED ANTENNA & LNA

## Slide 6: MAIN OPERATING CONSOLE

## Slide 7: ANTENNA TRACKING CONSOLE

## Slide 8: EQUIPMENT USED

## Slide 9: SUMMARY OF RECORDED DATA
Total of 14.04 hours of data was recorded throughout all nights.
2026-04-04 (the longest session) → 8.04 hours
2026-04-04 (second session) → 0.45 hours
2026-04-08 → 2.31 hours
2026-04-09 (early session) → 2.16 hours
2026-04-09 (later session) → 1.08 hours

## Slide 10: FIRST DETECTION
First detected signal from ORION spacecraft was observed on 04-04-2026 at 06:28:39 UTC (00:28:39 MST)
Carrier signal
The SNR was 23.3dB with peak up to 26dB, stable and easily trackable.
The measured Doppler shift was -7.517kHz with reassured transmitted frequency of 2216.492483 MHz

## Slide 11: OBSERVATION RESULTS
Doppler Behavior
Across all sessions:
- Doppler exhibits smooth monotonic drift
- Typical drift rate:
~ +0.04 to +0.05 Hz/s
Matches expected:
  Increasing radial velocity from Earth
  Translunar trajectory dynamics
Signal Detection
- Strong, continuous carrier lock
- No major dropouts
- Stable SNR across most integrations
The highest SNR recorded 26dB The lowest SNR recorded 16dB
Furthest point was ~ 355,000km

## Slide 12: SUMMARY OF RECORDED DATA
April 4th Data
Noise: 41–136 Hz
Drift: –30 to –600 Hz
Timing jitter: ~10–25 ms
April 8th Data
Noise: ~170 Hz
Drift: –622 Hz
Timing jitter: ~0.8 sec
April 9th Data
Noise: ~135-145 Hz
Drift: –386 to -531 Hz
Timing jitter: ~27-28 ms

## Slide 13: DATA QUALITY ASSESMENT
Strengths
1. Excellent Doppler slope fidelity
Measured slope matches JPL predictions very closely
Indicates:
  Correct frequency reference scaling
  Proper Doppler extraction logic
2. High temporal continuity
Continuous tracking across sessions
Minimal gaps
3. Low random noise
Doppler jitter is small
Suitable for:
  Velocity estimation
  Residual analysis

## Slide 14: ISSUES IDENTIFIED
Baseline Offset Discontinuities
Sudden jumps (~50–150 Hz)
Then recovery to original trend
Interpretation:
NOT physical Doppler
Instrument/system-induced
Likely causes:
SDR LO retuning or reinitialization
Reference (10MHz) phase reset
Peak-tracking ambiguity
DC notch interaction
Segment-dependent bias
Each continuous segment has:
- Internally consistent slope
- But different absolute offset
Indicates:
Reference drift OR
Tracking reacquisition bias
dominant systematic error

## Slide 15: ERROR VISUALIZATION USING GQRX
Recorded RAW IQ DATA
ORION CARRIER

## Slide 16: EXAMPLE OF DOPPLER EXTRACTION

## Slide 17: ANOTHER EXAMPLE

## Slide 18: EXAMPLE OF GOOD DATA

## Slide 19: COMPARISON WITH JPL PREDICTION
Using Horizons ephemeris:
- Range-rate increases smoothly (positive acceleration)
- Measured Doppler slope matches:
Agreement:
- Trend
- Curvature
- Sign
Discrepancy:
Absolute offset varies between segments

## Slide 20: APRIL 4th DOPPLER DATA
APRIL 4th DATA

## Slide 21: APRIL 4th DOPPLER DATA
APRIL 4th DATA
APRIL 4th DATA

## Slide 22: APRIL 4th DOPPLER DATA
APRIL 4th DATA
APRIL 4th DATA
APRIL 8th DATA

## Slide 23: APRIL 4th DOPPLER DATA
APRIL 4th DATA
APRIL 4th DATA
APRIL 8th DATA
APRIL 9th DATA

## Slide 24: APRIL 4th DOPPLER DATA
APRIL 4th DATA
APRIL 4th DATA
APRIL 8th DATA
APRIL 9th DATA
APRIL 9th DATA

## Slide 25: ARTEMIS-II DOPPLER LOGGER

## Slide 26: OUTPUT FORMAT CCSDS TDM v2.0
CCSDS_TDM_VERS = 2.0 ORIGINATOR = DSES CREATION_DATE = 2026-04-04T14:31:18.160Z META_START TIME_SYSTEM = UTC PARTICIPANT_1 = ORION PARTICIPANT_2 = DSES MODE = SEQUENTIAL PATH = 1,2 INTEGRATION_INTERVAL = 1.000000 INTEGRATION_REF = END FREQ_OFFSET = 2216500000.000 START_TIME = 2026-04-04T06:28:39.890Z STOP_TIME = 2026-04-04T14:31:17.159Z TURNAROUND_NUMERATOR = 240 TURNAROUND_DENOMINATOR = 221 META_STOP
DATA_START RECEIVE_FREQ_2 = 2026-04-04T06:28:39.890Z 2216492804.299 RECEIVE_FREQ_2 = 2026-04-04T06:28:40.152Z 2216492791.508 RECEIVE_FREQ_2 = 2026-04-04T06:28:40.566Z 2216492796.558 RECEIVE_FREQ_2 = 2026-04-04T06:28:40.909Z 2216492780.814 RECEIVE_FREQ_2 = 2026-04-04T06:28:41.226Z 2216492776.523 RECEIVE_FREQ_2 = 2026-04-04T06:28:41.400Z 2216492792.109 RECEIVE_FREQ_2 = 2026-04-04T06:28:41.683Z 2216492806.615 RECEIVE_FREQ_2 = 2026-04-04T06:28:41.940Z 2216492780.829 RECEIVE_FREQ_2 = 2026-04-04T06:28:42.198Z 2216492776.729 RECEIVE_FREQ_2 = 2026-04-04T06:28:42.456Z 2216492774.341 DATA_STOP

## Slide 27: OVERALL DATA QUALITY
Metric | Rating
Doppler slope accuracy | ⭐⭐⭐⭐⭐ (Excellent)
Noise / stability | ⭐⭐⭐⭐☆ (Very good)
Continuity | ⭐⭐⭐⭐☆ (Very good)
Absolute accuracy | ⭐⭐☆☆☆ (Poor)
DSN-grade usability | ⭐⭐⭐☆☆ (Good)
“This is a first-of-its-kind DSES effort”

## Slide 28: KEY TECHNICAL INSIGHT
This dataset shows:
Our system is dynamically correct but not absolutely referenced continuously
Meaning:
Physics = correct
Measurement = precise
Reference = discontinuous (that include software and hardware)

## Slide 29: SCIENTIFIC VALUE
Despite offset issues, this dataset is:
Valid for:
- Doppler slope / velocity estimation
- Trajectory verification
- Educational DSN-style experiments
Limited for:
- Absolute frequency comparison
- High-precision orbit determination

## Slide 30: FINAL CONCLUSION
The ARTEMIS-II Doppler tracking campaign demonstrates:
High-quality Doppler tracking capability with excellent dynamic fidelity, limited primarily by reference discontinuities rather than signal or processing limitations.
With minor improvements, our system can reach:
Near-DSN-quality Doppler performance

## Slide 31: QUESTIONS ?